## Slide 1
DESIGN-AWARE
UAV Path Planning
How Mechanical Design Influences Mission Optimization
Presenter Name | UAV Autonomous Systems Project | 2025

## Slide 2
02 / PROBLEM STATEMENT
The Gap in Current UAV Planning
1
Fixed Drone Model
Current planners assume all drones are identical — design differences are completely ignored.
2
One-Size-Fits-All Paths
The same path is applied to radically different drones, ignoring their physical constraints.
3
Cascading Inefficiency
Results in unrealistic trajectories, energy waste, and mission failures in the field.
GOAL Build a planner that adapts to each drone's physical design, producing realistic and efficient missions.

## Slide 3
03 / CORE IDEA
Design → Physics → Optimal Mission
INPUT
Drone Design
Parameters
• Rotor count • Total mass • Propeller size • Battery capacity
PROCESS
Physics +
Constraints
• Flight envelope • Energy model • Turn radius • Speed limits
OUTPUT
Optimal Path
& Speed
• Cruise speed • Flight altitude • Coverage path • Total energy

## Slide 4
04 / KEY DESIGN PARAMETERS
What Defines Flight Capability
01
Rotor Count
3, 4, 6 or 8 motors
Defines stability and control authority
02
Total Mass
Frame + payload + battery
Directly drives required thrust
03
Propeller Size
Diameter & pitch
Determines aerodynamic efficiency
04
Motor Characteristics
KV rating, efficiency curve
Sets power draw at given throttle
05
Battery Capacity
Voltage × Ah
Hard ceiling on total mission energy

## Slide 5
05 / ROTOR CONFIGURATION
Same Mission ≠ Same Optimal Path
TRICOPTER
3 Rotors
Less stable yaw control
Requires larger turn radius
Lower cruise speed limit
Suited for lightweight payloads
QUADCOPTER
4 Rotors
Balanced, stable platform
Efficient for area mapping
Higher achievable cruise speed
Preferred for most missions

## Slide 6
06 / MASS, PAYLOAD & POWER
The Weight–Energy Cascade
1
Higher Mass
Heavier frame + payload load
2
Greater Thrust Required
Motors must work harder to stay aloft
3
Power Consumption Rises
P ∝ T^(3/2) — non-linear relationship
4
Shorter Flight Time
Battery depletes faster
5
Reduced Mission Coverage
Smaller area can be surveyed per flight
Power–Thrust Relation
P ∝ T ^(3/2)
Key Takeaways
Payload planning is not optional
Mass must be minimized where possible
Power model must be non-linear

## Slide 7
07 / ENERGY MODEL
Flying Smart, Not Just Fast
Total Power: P = P_induced + P_drag
Induced Power
P_ind ∝ T^(3/2)
Power required to generate lift against gravity. Dominant at low speeds.
Drag Power
P_drag ∝ V³
Power expended overcoming aerodynamic drag during forward flight. Grows with V³.
OPTIMAL SPEED = min( P / V ) — minimise energy per unit distance, not total power

## Slide 8
08 / FLIGHT ENVELOPE & PATH PLANNING
What the Drone Can Physically Do
FLIGHT ENVELOPE
1
Max Speed
Hard ceiling from drag & stability
2
Max Tilt Angle
Limits horizontal acceleration & turning
3
Min Turn Radius
R = V² / (g · tan θ)
4
Battery Reserve
20–30% kept for RTH safety margin
COVERAGE STRATEGY
Lawnmower Pattern
Area divided into parallel sweeps, each obeying turn radius and speed constraints derived from the drone's physical model.
Altitude & Camera Link
spacing = 2h · tan(FOV/2) · (1 − overlap)
Higher altitude → wider footprint → fewer passes needed

## Slide 9
09 / SYSTEM ARCHITECTURE
The Core Contribution Pipeline
Drone
Design
Physics
Model
Flight
Envelope
Energy
Model
Path
Generator
Optimizer
Output
Input: Drone design parameters (mass, rotors, propellers, battery) | Process: Physics → constraints → optimisation loop | Output: Optimal speed, altitude, path, energy budget

## Slide 10
10 / OUTPUTS & APPLICATIONS
What the System Produces
Cruise Speed
m/s
Turn Radius
meters
Flight Altitude
AGL
Sweep Spacing
meters
Total Energy
Wh
Mission Time
minutes
APPLICATIONS
Surveying & Mapping
Precision Agriculture
Infrastructure Inspection
Autonomous Drone Deployment

## Slide 11
11 / CONCLUSION
Path Planning Must Be Physics-Aware
Design Matters
Mechanical design directly impacts what a drone can realistically achieve on a mission.
Ignoring It Costs
Generic path planners produce inefficient, unrealistic, and energy-wasteful trajectories.
Our Approach Wins
Design-aware planning improves realism, performance, and energy efficiency.
CORE CONTRIBUTION
A unified framework linking drone mechanical design to mission-level path optimization using physics-based constraints.

## Slide 12
12 / FUTURE WORK
Expanding the Framework
NEAR TERM
Wind-aware path planning
Adaptive speed control during flight
MID TERM
Multi-drone coordination & task splitting
Real-time obstacle avoidance integration
LONG TERM
AI/ML-based optimization (RL agents)
Hardware-in-the-loop simulation & validation